## Slide 1
Nanopore only Telomere-2-Telomere Assemblies for Genomes of Europe
ESHG 2025, Milano Caspar Gross

## Slide 2: Introduction
University Hospital Tübingen
Institute of Medical Genetics and Applied Genomics

## Slide 3: T2T Assemblies as part of Genomes of Europe
28 Institutes from Europe Sequencing goal: 500 000 genomes
At UKT:
Planned 20 000 genomes
Twin Study (n = 400 pairs) WGS-LR
T2T Genomes
T2T genomes sampled mainly from institute members, aiming for broad ethnic background.

## Slide 4: Human reference genomes
2001 First Draft Human Genome
2011 hg19 Reference Genome
2017 hg38 Reference Genome
2022 T2T-CHM13 First T2T Genome (haploid)
2023 The Human Pangenome Project
2024 HG002v1.1 Q77.8
2022 HG002v0.7 Q60
2024 Improved Methods
Herro (Stanojevic et al.)
ONT only (Koren et al)
2025 Publications
Hifiasm (Cheng et al)
6 T2T Ape (Yoo et al)
18 T2T Human (Ghorbani et al)

## Slide 5
> For an assembly to be truly T2T, it must both cover the whole of each chromosome without gaps and be free from large-scale assembly errors. It is critical to rigorously assess the quality of the assembly before concluding it is T2T.
Li and Durbin, 2024. “Genome Assembly in the Telomere-to-Telomere Era.” Nature Reviews Genetics

## Slide 6: Lab
Ultra-Long DNA
Sequencing Kit
SQK-ULK114
~45X with >=100kb N50
Assembly Polishing
Kit (APK)
SQK-APK114
>=35X with ~6-8 kb N50
Pore-C protocol with
Ligation Sequencing Kit
SQK-LSK114
Chromatin conformation capture data
>=25X with ~8kb N50
Chromosome correction data
Ultra-long reads (>=100kb)
1 lib prep on 1 flow cell
1 lib prep on 1 flow cell
2 lib preps on 3/4 flow cells

## Slide 7: Pore-C sequencing
3 days protocol
Can be generated from UHMW DNA
https://nanoporetech.com/sites/default/files/s3/literature/plant-pore-c-workflow.pdf
Notes: How does Pore-C work?
Chromatin is crosslinked in cells to preserve 3D structure.
DNA is fragmented and proximity-ligated, joining together DNA segments that are spatially close in the nucleus.
The resulting chimeric DNA molecules (containing multiple genomic fragments) are sequenced using Oxford Nanopore’s long-read technology.
Each read can contain information about multiple interacting genomic loci, providing high-resolution insight into chromatin organization.

## Slide 8: UL sequencing

## Slide 9: APK sequencing
Custom protocol

## Slide 10: Pipeline overview
Basecalling with SUP model on GPU nodes

## Slide 11: Basecalling, Error correction, Filtering
  HQ:
    Max 50x coverage
    >Q9
    Length priority
  UL:
    Max 70x coverage
    > Q9
    >80kb Length

## Slide 12: Input optimizations
2 UHMW Library Preps -> Enough for 14 Flowcell loadings
3 UL Flowcells
Duplex reads do not help
#TODO Figure

## Slide 13: Runtimes

## Slide 14: Assembly graph visualisation
Primary assembly, unphased, not scaffolded
Acrocentric chromosomes cluster at repetitive sequences
Sex chromosomes only single stranded (haploid)
chr22
chr15
chr14
chr13
chr2
chr4
chr6
chr11
chr12
chr3
chr1
chrY
chr7
chr5
chr9
chr17
chr10
chr8
chrX
chr19
chr20
chr16
chr18
GE-MED-T2T00
chr21

## Slide 15: Assembly graph visualisation
Phasing selects separate paths through the graph for each haplotype
Using Pore-C or Trio information.
Haplotype1: Red Haplotype2: Blue

## Slide 16: Assembly QC
Metric | haplotype1 | haplotype2
Number of T2T chromosomes | 20 | 18
% of Assembly covered by Ref | 0.97 | 0.97
% of Ref covered by Assembly | 0.9 | 0.94
% of Ref duplicated in Assembly | 0.01 | 0.01
Assembly Length | 2934985356 | 3028541959
Average Ungapped Alignment length | 4167916 | 4482112
Genome Completeness (%) | 94.61 | 98.41
Missing Multi-Copy Genes (%) | 0.19 | 0.22
NG50 | 137904320 | 145923310
NG75 | 101150053 | 103627408
 | complete assembly | 
Phase Blocks | 46 | 
Switch Rate (%) | 1.23 | 
Quality Value | 58.48 | 
Error Rate (%) | 0.00014 | 
Variants Phased (%) | 98.7 | 

## Slide 17: APK Polishing
#todo Add quality values

## Slide 18: Alignment against reference genome
Image 2 Tracks, Methylation included
#todo

## Slide 19: Extended QC
Nucflag
Gapstats

## Slide 20: Repeat analysis
Annotation of assembled genomes with RepeatMasker

## Slide 21: Contributors
Elena Buena-Atienza
Nanopore Sequencing
Ramya Potabattula
Ultra-Long Reads
Fubo Cheng
Pore-C
Prithivi Jung Thapa
Bioinformatics
Download: - Raw data - Assemblies
https://www.elrin-network.eu/t2t.html
Beate Kristmann
Project Management
Nicolas Casadei
NCCT, Core facility
Olaf Riess
Project Lead
Stephan Ossowski
Head of Bioinformatics
Hanna Sophie Hartung
Nanopore Sequencing

## Slide 22: Hifiasm (Additional slide)
No support for Pore-C yet
#todo insert QC